## Slide 1
WELCOME! TO CAMPUS CHAM

## Slide 2
CAMPUS CHAM
Author: Team Fire
Cham
Energy Optimization of e-VTOL systems using Simulation-Based Analysis

## Slide 3
Introduction
System Inefficiencies
Non-Optimized System Weight
Unnecessary Energy Consumption
Flight Time
More Expensive Battery Pack

## Slide 4
Aim & Objectives
What Do We Plan to Achieve?
Lower budget motor-battery package
Less energy for the same distance
More efficient e-vtol systems
Lighter e-vtol systems

## Slide 5
System Description
MX860 Vertical Take-Off and Landing

## Slide 6
System Specifications
Specification | Value
Max Take-off Weight | 19.96 kg
Weight (with Battery) | 9.96 kg
Battery | 2 × 6S 30Ah 22.2 V (Total: 60Ah, 5.2 kg)
Hover Time ( 9 kg) | 24 minutes
Motor Configuration | 8 × T-MOTOR MN6007 KV320

## Slide 7
Simulink Model Architecture

## Slide 8
Simulation Outputs Flight Time vs Total Weight (Ares)

## Slide 9
Simulation Outputs Flight Time vs Hover Thrust (Ares)

## Slide 10
Simulation Outputs Flight Time vs Total Weight (XTAR)

## Slide 11
Simulation Outputs Flight Time vs Hover Thrust (XTAR)

## Slide 12
Simulation Outputs Flight Time vs Total Weight (Keeppower)

## Slide 13
Simulation Outputs Flight Time vs Hover Thrust (Keeppower)

## Slide 14
The Algorithm of Optimization
Output

## Slide 15
System Specifications
Specif. | Value |  | 
Battery Name | Keeppower | XTAR | Ares Base Model
Battery Weight | 49x6x18= 5292 gr | 51x6x17= 5202 gr | 2600x2= 5200 gr
Battery Capacity | 68.4 Ah | 61.2 Ah | 60.0 Ah
Battery | 18 x 6S 22.2 V | 17 x 6S 22.2 V | 2 × 6S 22.2 V

## Slide 16
Analysis of energy inefficiencies
Specif. | Value |  | 
Battery Name | Keeppower | XTAR | Ares Base Model
Hover Time ( 9 kg) | 28.1 | 25.2 | 24.7
Flight Time is for the same battery weight |  |  | 
Flight Time Improvement Percentage | 13.77% | 2.02% | 24.7
Or energy use is for the same flight duration |  |  | 
Energy Utilization | 1181 Wh 11.3% | 1278 Wh 4.05% | 1332 Wh

## Slide 17
Future Scope
Batteries with higher energy capacity
Current battery energy density averages around 250–300 Wh/kg, with expectations to reach 400 Wh/kg in 5 years and up to 500–600 Wh/kg in 10 years through advancements.
Advanced AI support
With advanced AI algorithms, more efficient and adaptive flight profiles can be generated based on real-time payload, mission type, and battery status.
Next-Gen Power Technologies
Future integration of alternative energy sources such as hydrogen fuel cells and nuclear batteries could significantly extend flight endurance and reduce reliance on conventional lithium-based systems.
Modular Power Systems
Designing swappable battery/motor modules to adapt the aircraft for different missions and payloads.

## Slide 18
Project Plan
📅 30.04.2025 ➔ Concept Presntation (TASK 1)
📅 01.05.2025 – 10.05.2025
➔ Component Library Creation (Weight, Energy Capacity, Power Consumption, Price)
📅 11.05.2025 – 20.05.2025 ➔ Simulation of Example System (Motor Selection, Battery Matching, Energy Consumption Calculation, Visualization)
📅 21.05.2025 ➔ System Simulation Presentation (TASK 2)

## Slide 19
Project Plan
📅 22.05.2025 – 10.06.2025
➔ Optimization Model Development
📅 11.06.2025 – 17.06.2025
➔ Final Simulation and Comparison
📅 18.06.2025
➔ Final Presentation (TASK 4)
📅 01.06.2025 – 01.07.2025
➔ Report Writing (IEEE Format)

## Slide 20
References
Data Source: T-MOTOR Official Website – MN6007 KV320 Datasheet and Ares Battary
Data Source: Keeppower 18650 3800mAh Specification Sheet
Data Source: XTAR 18650 3600mAh Specification Sheet
H. Taghbalout, L. A. Doustmohammadi, M. Shahbakhti, "Energy Management of an eVTOL Aircraft with Optimization-Based Powertrain Control," 2024 IEEE Transactions on Transportation Electrification, 2024.
P. Chatterjee, A. Ray, and S. Kar, “Electric Vehicle Modeling in MATLAB and Simulink with SoC SoE Estimation of a Lithium-ion Battery,” IOP Conf. Series: Journal of Physics: Conf. Series, vol. 2385, no. 1, 2022.

## Slide 21
THANK YOU